## Slide 1: جبر بول
Boolean Algebra

## Slide 2: جبر بول
قوت اصلي سيستم هاي ديجيتال:
  جامعيت و قدرت فرمولاسيون رياضي جبر بول
مثال:
IF the lift door is closed
AND a button is pressed at a floor
THEN the lift must move
هر دو شرط:
the lift door is closed و
a button is pressed at a floor بايد true باشند تا آسانسور حرکت کند.

## Slide 3: Digital Systems: Boolean Algebra and Logical Operations
In Boolean algebra:
  Values: 0,1
  0: if a logic statement is false,
  1: if a logic statement is true.
Operators: AND, OR, NOT

## Slide 4: مثال
IF the lift door is closed
AND a button is pressed at a floor
THEN the lift must move
door closed?
button pressed?
move lift?
false/0
false/0
true/1
true/1
false/0
true/1
false/0
true/1
false/0
false/0
false/0
TRUE/1

## Slide 5: سيستم هاي نوعي
ورودي ها:
  فشار کليد (ديجيتال)
  درجةحرارت محيط (آنالوگ)
  تغييرات سطح مايع (آنالوگ)
خروجي ها:
  ولتاژ راه اندازي موتور (آنالوگ)
  بازکردن/بستن شير (آنالوگ يا ديجيتال)
  نمايش روي LCD (ديجيتال)
System

## Slide 6: سيستم هاي نوعي
ورودي ها:
  فشار کليد (ديجيتال)
  درجةحرارت محيط (آنالوگ)
  تغييرات سطح مايع (آنالوگ)
خروجي ها:
  ولتاژ راه اندازي موتور (آنالوگ)
  بازکردن/بستن شير (آنالوگ يا ديجيتال)
  نمايش روي LCD (ديجيتال)
Digital System
Analog Phenomena
Digital Inputs
A2D
Sensors & other inputs
Analog Inputs
Digital Inputs
Digital Outputs
Digital Outputs
D2A
Actuators and Other Outputs
System

## Slide 7: مثال: دستگاه اطفاي حريق خودکار
Digital System
Analog Phenomena
Digital Inputs
A2D
Sensors & other inputs
Analog Inputs
Digital Inputs
Digital Outputs
Digital Outputs
D2A
Actuators and Other Outputs
رفتار سيستم:
  اگر درجة حرارت محيط از مقدار مشخصي بيشتر است و کليد فعال سازي دستگاه روشن است، شير آب را باز کن.
System

## Slide 8: مثال: چراغ هشدار کمربند ايمني
  S = ‘1’: کمربند بسته است.
  K = ‘1’: سوييچ داخل است.
  P = ‘1’: راننده روي صندلي است.
Digital System
Analog Phenomena
Digital Inputs
A2D
Sensors & other inputs
Analog Inputs
Digital Inputs
Digital Outputs
Digital Outputs
D2A
Actuators and Other Outputs

## Slide 9: سوييچ ها: عملگرهاي منطقي
IF the lift door is closed
AND a button is pressed at a floor
AND “Open” button is off
THEN the lift must move
T
rue
Move lift
Button
pressed
Open
off
Door
closed
Open button

## Slide 10: سوييچ ها: عملگرهاي منطقي
IF ((a button pressed at a floor
AND “Open” button is off)
OR a button inside the lift is pressed)
AND the door lift is closed
THEN the lift can move
Open
Is off
Door
closed
True
True
Move lift
Button
at a floor
Button
inside
IF the lift door is closed
AND a button is pressed at a floor
AND “Open” button is off
THEN the lift must move
T
rue
Move lift
Button
pressed
Open
off
Door
closed
Open button

## Slide 11: Binary Logic
  Deals with binary variables that take 2 discrete values (0 and 1), and with logic operations
  Basic logic operations:
    AND, OR, NOT
  Binary/logic variables: letters: A,B,C,…,X,Y,Z

## Slide 12: Binary Logic Function
F(vars) = expression
Example:
F(a,b) = a’•b + b’
G(x,y,z) = x•(y+z’)
set of binary
variables
Operators ( +, •, ‘ )
Variables
Constants ( 0, 1 )
Groupings (parenthesis)

## Slide 13: Basic Logic Operators
  AND (also •, )
  OR (also +, )
  NOT (also ’, )
  F(a,b) = a•b, reads F is 1 if and only if a=b=1
  G(a,b) = a+b, reads G is 1 if either a=1 or b=1 or both
  H(a) = a’, reads H is 1 if a=0
Binary
Unary

## Slide 14: Basic Logic Operators (cont.)
1-bit logic AND resembles binary multiplication:
  0 • 0 = 0, 0 • 1 = 0,
  1 • 0 = 0, 1 • 1 = 1
1-bit logic OR resembles binary addition, except for one operation:
  0 + 0 = 0, 0 + 1 = 1,
  1 + 0 = 1, 1 + 1 = 1 (≠ 102)

## Slide 15: Truth Tables for logic operators
Truth table:
tabular form that uniquely represents the relationship between the input variables of a function and its output
A | B | F=A•B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
2-Input AND
A | B | F=A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
2-Input OR
A | F=A’
0 | 1
1 | 0
NOT

## Slide 16: Truth Tables (cont.)
Q:
  Let a function F() depend on n variables. How many rows are there in the truth table of F() ?

## Slide 17: Truth Tables (cont.)
Q:
  Let a function F() depend on n variables. How many rows are there in the truth table of F() ?
A:
  2n rows, since there are 2n possible binary patterns/combinations for the n variables

## Slide 18: Logic Gates
  Logic gates are abstractions of electronic circuit components that operate on one or more input signals to produce an output signal.
2-Input AND
2-Input OR
NOT (Inverter)
A
A
A
B
B
F
G
H
F = A•B
G = A+B
H = A’

## Slide 19: Timing Diagram
A
B
F=A•B
G=A+B
H=A’
1
1
1
1
1
0
0
0
0
0
t0
t1
t2
t3
t4
t5
t6
Input
signals
Gate
Output
Signals
Basic
Assumption:
Zero time for
signals to
propagate
Through gates
Transitions

## Slide 20: The Real World
  Intermediate values may be visible for an instant
  Boolean algebra useful for describing the steady state behavior of digital systems
  Be aware of the dynamic, time varying behavior too!
  Physical electronic components are continuous, not discrete!
    Transition from logic 1 to logic 0 does not take place instantaneously in real digital systems
  These are the building blocks of all digital components!
Time

## Slide 21: Circuit that implements logical negation (NOT)
Inverter behavior as a function of input voltage
input ramps from 0V to 5V
output holds at 5V for some range of small input voltages
then changes rapidly, but not instantaneously!
V
Out
+5
0
+5
V
In
Logic 0 Input
Voltage
Logic 1 Input
Voltage

## Slide 22: Logic Gates
Steady state matters in Boolean algebra

## Slide 23: Three-Input Gates

## Slide 24: Combinational Logic Circuit from Logic Function
Combinational Circuit Design:
F = A’ + B•C’ + A’•B’
  connect input signals and logic gates:
    Circuit input signals  from function variables (A, B, C)
    Circuit output signal  function output (F)
    Logic gates  from logic operations

## Slide 25: Combinational Logic Circuit from Logic Function
Combinational Circuit Design:
F = A’ + B•C’ + A’•B’
  connect input signals and logic gates:
    Circuit input signals  from function variables (A, B, C)
    Circuit output signal  function output (F)
    Logic gates  from logic operations
A
B
C
F

## Slide 26: Logic Evaluation
Logic Expression :
Circuit of logic gates :

## Slide 27: Logic Evaluation
Logic Expression :
Circuit of logic gates :

## Slide 28: Logic Evaluation
Logic Expression :
Circuit of logic gates :
Logic Evaluation : A=B=C=1, D=E=0

## Slide 29: Logic Evaluation
Logic Expression :
Circuit of logic gates :
Logic Evaluation : A=B=C=1, D=E=0

## Slide 30: Logic Evaluation
Logic Evaluation : A=B=C=1, D=E=0

## Slide 31: Combinational Logic Optimization
  In order to design a cost-effective and efficient circuit, we must minimize
    the circuit’s size
      area
    propagation delay
      time required for an input signal change to be observed correctly at the output line

## Slide 32: Combinational Logic Optimization
  In order to design a cost-effective and efficient circuit, we must minimize
    the circuit’s size
      area
    propagation delay
      time required for an input signal change to be observed correctly at the output line
  Observe the truth table of
    F = A’ + B•C’ + A’•B’
    G = A’ + B•C’
  are identical  same function
  Use G to implement the logic circuit
    less components
A | B | C | F | G
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0

## Slide 33: Proof Using Truth Table
n variable needs rows
n times
A B C |  | B’ | AB’ | AB’ + C |  | A + C | B’ + C | (A + C) (B’ + C)
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 |  | 1 1 0 0 1 1 0 0 | 0 0 0 0 1 1 0 0 | 0 1 0 1 1 1 0 1 |  | 0 1 0 1 1 1 1 1 | 1 1 0 1 1 1 0 1 | 0 1 0 1 1 1 0 1

## Slide 34: Combinational Logic Optimization
A
B
C
F
A
B
C
G
    F=A’ + B•C’ + A’•B’
    G=A’ + B•C’

## Slide 35: Boolean Algebra
  VERY nice machinery used to manipulate (simplify) Boolean functions
  George Boole (1815-1864): “An investigation of the laws of thought”
  Terminology:
    Literal: A variable or its complement
      A, B’, x’
    Product term: literals connected by •
      X.Y
      A.B’.C.D,
    Sum term: literals connected by +
      A+B’
      A’+B’+C

## Slide 36: Boolean Algebra Properties
Let X: boolean variable,
0,1: constants
  X + 0 = X -- Zero Axiom
  X • 1 = X -- Unit Axiom
  X + 1 = 1 -- Unit Property
  X • 0 = 0 -- Zero Property
A | B | F=A•B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | F=A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Example:

## Slide 37: Boolean Algebra Properties (cont.)
Let X: boolean variable,
0,1: constants
  X + X = X -- Idempotent
  X • X = X -- Idempotent
  X + X’ = 1 -- Complement
  X • X’ = 0 -- Complement
  (X’)’ = X -- Involution
A | B | F=A•B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | F=A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Example:

## Slide 38: The Duality Principle
  The dual of an expression is obtained by exchanging (• and +), and (1 and 0) in it,
    provided that the precedence of operations is not changed.
  Do not exchange x with x’
  Example:
    Find H(x,y,z), the dual of F(x,y,z) = x’yz’ + x’y’z

## Slide 39: The Duality Principle
  The dual of an expression is obtained by exchanging (• and +), and (1 and 0) in it,
    provided that the precedence of operations is not changed.
  Do not exchange x with x’
  Example:
    Find H(x,y,z), the dual of F(x,y,z) = x’yz’ + x’y’z
    H = (x’+y+z’) (x’+y’+ z)
  Dual does not always equal the original expression
If a Boolean equation is valid, its dual is also valid

## Slide 40: The Duality Principle (cont.)
  With respect to duality, Identities 1 – 8 have the following relationship:
1. X + 0 = X 2. X • 1 = X (dual of 1)
3. X + 1 = 1 4. X • 0 = 0 (dual of 3)
5. X + X = X 6. X • X = X (dual of 5)
7. X + X’ = 1 8. X • X’ = 0 (dual of 8)

## Slide 41: More Boolean Algebra Properties
Let X,Y, and Z: boolean variables
10. X + Y = Y + X 11. X • Y = Y • X -- Commutative
12. X + (Y+Z) = (X+Y) + Z 13. X•(Y•Z) = (X•Y)•Z -- Associative
14. X•(Y+Z) = X•Y + X•Z 15. X+(Y•Z) = (X+Y) • (X+Z) -- Distributive
16. (X + Y)’ = X’ • Y’ 17. (X • Y)’ = X’ + Y’ -- DeMorgan’s
In general,
( X1 + X2 + … + Xn )’ = X1’•X2’ • … •Xn’
( X1•X2•… •Xn )’ = X1’ + X2’ + … + Xn’

## Slide 42: Associative Laws for AND
A
A(BC)=ABC
=
A
B
C
C
B

## Slide 43: Proof of Associative Law
Associative Laws:
X Y Z |  | XY YZ | (XY)Z X(YZ)
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 |  | 0 0 0 0 0 0 0 1 0 0 0 0 1 0 1 1 | 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 1
Proof of Associative Law for AND

## Slide 44: Distributive Law
Distributive Laws:
Valid only for Boolean algebra not for ordinary algebra
Proof of the second law:
(A+B).C = A.C + B.C
(X + Y)(X + Z) =

## Slide 45: Distributive Law
Distributive Laws:
Valid only for Boolean algebra not for ordinary algebra
Proof of the second law:
(A+B).C = A.C + B.C
C

## Slide 46: Absorption Property (Covering)
  x + x•y = x
  x•(x+y) = x (dual)
Proof: x + x•y

## Slide 47: Absorption Property (Covering)
  x + x•y = x
  x•(x+y) = x (dual)
Proof: x + x•y = x•1 + x•y = x•(1+y) = x•1 = x QED (2 true by duality)

## Slide 48: Absorption Property (Covering)
  x + x’•y = x + y
  x•(x’+y) = x y (dual)
Proof of 2: x • (x’+ y) =

## Slide 49: Absorption Property (Covering)
  x + x’•y = x + y
  x•(x’+y) = x y (dual)
Proof of 2: x • (x’+ y) = x•x’ + x•y = 0 + (x•y) = x•y QED (1 true by duality)

## Slide 50: DeMorgan’s Laws
X Y |  | X’ Y’ | X + Y | ( X + Y )’ | X’ Y’ |  | XY | ( XY )’ | X’ + Y’
0 0 0 1 1 0 1 1 |  | 1 1 1 0 0 1 0 0 | 0 1 1 1 | 1 0 0 0 | 1 0 0 0 |  | 0 0 0 1 | 1 1 1 0 | 1 1 1 0
Proof
DeMorgan’s Laws for n variables
Example

## Slide 51: Consensus Theorem
  xy + x’z + yz = xy + x’z
  (x+y)•(x’+z)•(y+z) = (x+y)•(x’+z) -- (dual)
  Proof: xy + x’z + yz

## Slide 52: Consensus Theorem
  xy + x’z + yz = xy + x’z
  (x+y)•(x’+z)•(y+z) = (x+y)•(x’+z) -- (dual)
  Proof: xy + x’z + yz = xy + x’z + (x+x’)yz = xy + x’z + xyz + x’yz = (xy + xyz) + (x’z + x’zy) = xy + x’z QED (2 true by duality).

## Slide 53: Consensus Theorem
Example:

## Slide 54: Consensus Theorem
Example:

## Slide 55: Consensus Theorem
Example:

## Slide 56: Consensus Theorem
Reducing an expression
by adding a term and eliminate.
Example:

## Slide 57: Consensus Theorem
Reducing an expression
by adding a term and eliminate.
Consensus
Term added
Final expression
Example:

## Slide 58: Algebraic Manipulation
  Boolean algebra is a useful tool for simplifying digital circuits.
  Why do simplification?
    Simpler can mean cheaper, smaller, faster
Reduce number of literals (gate inputs; fan-in)
- Limited in some technologies
- Larger circuit
- Slower
• Reduce number of gates
- influences manufacturing costs
• Reduce number of levels of gates
- Reduced signal propagation delays

## Slide 59: Levels of Gates
Number of levels:
  From inputs to outputs

## Slide 60: Algebraic Simplification
2. Adding terms using
1. Combining terms
Example:
Example:
3. Eliminating terms
Example:
Example:
Example:

## Slide 61: Algebraic Manipulation
  Example: Simplify F = x’yz + x’yz’ + xz.
  F= x’yz + x’yz’ + xz
  = x’y(z+z’) + xz
  = x’y•1 + xz
  = x’y + xz
y
z
x
F
y
z
x
F

## Slide 62: Algebraic Manipulation (cont.)
  Example: Prove x’y’z’ + x’yz’ + xyz’ = x’z’ + yz’
  Proof: x’y’z’+ x’yz’+ xyz’
  = x’y’z’ + x’yz’ + x’yz’ + xyz’
  = x’z’(y’+y) + yz’(x’+x)
  = x’z’•1 + yz’•1
  = x’z’ + yz’
  QED.

## Slide 63: Sum of Products (SOP)
Sum of product form:
Still considered to be in sum of product form:
Not in Sum of product form:
Multiplying out and eliminating redundant terms

## Slide 64: Product of Sums (POS)
Product of sum form:
Still considered to be in product of sum form:

## Slide 65: Circuits for SOP and POS form
Sum of product form:
Product of sum form:

## Slide 66: Multiplying Out and Factoring
(3-3)
Y
X
XZ
Z
X
Y
X
'
)
'
)(
(
+
=
+
+
4
4
3
4
4
2
1
8
7
6
1,
X
If
=
0,
X
If
=
To obtain a sum-of-product form  Multiplying out using distributive laws
Theorem for multiplying out:

## Slide 67: Multiplying Out and Factoring
(3-3)
Y
X
XZ
Z
X
Y
X
'
)
'
)(
(
+
=
+
+
4
4
3
4
4
2
1
8
7
6
valid.
always
is
it
1,
X
and
0
X
both
for
valid
is
equation
the
because
=
=
Z.
or Z
Y
0
Z
Y)Z
(1
to
reduces
3)
-
(3
1,
X
If
=
*
+
=
+
=
Y.
Y
or
Y
1
0
Z)
Y(1
to
reduces
3)
-
(3
0,
X
If
=
*
+
=
+
=
To obtain a sum-of-product form  Multiplying out using distributive laws
Theorem for multiplying out:

## Slide 68: Multiplying Out and Factoring
(3-3)
Y
X
XZ
Z
X
Y
X
'
)
'
)(
(
+
=
+
+
4
4
3
4
4
2
1
8
7
6
valid.
always
is
it
1,
X
and
0
X
both
for
valid
is
equation
the
because
=
=
Z.
or Z
Y
0
Z
Y)Z
(1
to
reduces
3)
-
(3
1,
X
If
=
*
+
=
+
=
Y.
Y
or
Y
1
0
Z)
Y(1
to
reduces
3)
-
(3
0,
X
If
=
*
+
=
+
=
)
'
)(
(
'
B
A
C
A
C
A
B
A
+
+
=
+
4
3
4
2
1
8
7
6
To obtain a sum-of-product form  Multiplying out using distributive laws
Theorem for multiplying out:
The use of Theorem 3-3 for factoring:
Example:

## Slide 69: Multiplying out (Another Proof)
Theorem for multiplying out:
(3-3)
Y
X
XZ
Z
X
Y
X
'
)
'
)(
(
+
=
+
+
4
4
3
4
4
2
1
8
7
6

## Slide 70: Factoring Expressions
Y
X
XZ
'
DE
C
BE
BD
A
AC
)
'
'
(
'
+
+
+
=
DE
C
A
BE
A
BD
A
AC
'
'
'
'
'
+
+
+
Z
Y
X
C
A
E
D
B
DE
C
A
)
'
)](
'
(
'
[
+
+
+
+
=
C
A
DE
C
BE
BD
A
)
'
)(
'
'
(
+
+
+
+
=
)
'
)(
'
)(
)(
)(
'
(
C
A
E
D
A
E
B
A
D
B
A
C
B
A
+
+
+
+
+
+
+
+
+
=
)
'
)(
'
'
)(
'
(
C
A
E
D
DE
C
A
DE
C
B
A
+
+
+
+
+
+
=
To obtain a product-of-sum form  Factoring using distributive laws
Example of factoring:

## Slide 71: Conversion of English Sentences to Boolean Equations
  The first step in designing a logic network:
    Translate English sentences to Boolean Eqns.
      We must break down each sentence into phrases
      And associate a Boolean variable with each phrase (possible if a phrase can have a “true”/”false” value)
  Example:
    Turn on light if it is night and a movement is detected.
     F = A . B

## Slide 72: Main Steps
  Three main steps in designing a single-output combinational switching network:
    Find a switching function which specifies the desired behavior of the network.
    Find a simplified algebraic expression for the function.
    Realize the simplified function using available logic elements.

## Slide 73: Example
  Four chairs in a row:
    Occupied: ‘1’
    Empty: ‘0’
    F = ‘1’ iff there are no adjacent empty chairs.
A
B
C
D

## Slide 74: Example
  Four chairs in a row:
    Occupied: ‘1’
    Empty: ‘0’
    F = ‘1’ iff there are no adjacent empty chairs.
A
B
C
D
  F = (B’C’ + A’B’ + C’D’)’

## Slide 75: Example
  F = (B’C’ + A’B’ + C’D’)’
  F = (B+C).(A+B).(C+D)
  = (B+AC).(C+D)
  = BC + BD + AC + ACD
  = BC + BD + AC

## Slide 76: Truth Tables (revisited)
  Enumerates all possible combinations of variable values and the corresponding function value
  Truth tables for some arbitrary functions F1(x,y,z), F2(x,y,z), and F3(x,y,z) are shown to the right.
x | y | z |  | F1 | F2 | F3
0 | 0 | 0 |  | 0 | 1 | 1
0 | 0 | 1 |  | 0 | 0 | 1
0 | 1 | 0 |  | 0 | 0 | 1
0 | 1 | 1 |  | 0 | 1 | 1
1 | 0 | 0 |  | 0 | 1 | 0
1 | 0 | 1 |  | 0 | 1 | 0
1 | 1 | 0 |  | 0 | 0 | 0
1 | 1 | 1 |  | 1 | 0 | 1

## Slide 77: Truth Tables (cont.)
  Truth table: a unique representation of a Boolean function
  If two functions have identical truth tables, the functions are equivalent (and vice-versa).
  Truth tables can be used to prove equality theorems.
  However, the size of a truth table grows exponentially with the number of variables involved.
    This motivates the use of Boolean Algebra.

## Slide 78: آزمايشگاه
از هفته آینده
25% نمره کل 4 واحد
  کاملا در اختيار مدرس آزمايشگاه
قوانین مطالعه شود

## Slide 79: Circuit Analysis
  Circuit to be analyzed:

## Slide 80: Circuit Analysis
  Circuit to be analyzed:
  Consider all possible combinations of inputs

## Slide 81: Circuit Analysis
  Circuit to be analyzed:
  Can also name the nodes
N1
N2
N3
F = N2+N3
N1 = X+Y’
N2 = N1.Z
N3 = X’.Y.Z’
F = N1.Z+ X’.Y.Z’
= (X+Y’). Z+ X’.Y.Z’

## Slide 82: Boolean expressions- NOT unique
  Unlike truth tables, expressions representing a Boolean function are NOT unique.
  Example:
    F(x,y,z) = x’•y’•z’ + x’•y•z’ + x•y•z’
    G(x,y,z) = x’•y’•z’ + y•z’
  The corresponding truth tables for F() and G() are identical!
  Thus, F() = G()
x | y | z |  | F | G
0 | 0 | 0 |  | 1 | 1
0 | 0 | 1 |  | 0 | 0
0 | 1 | 0 |  | 1 | 1
0 | 1 | 1 |  | 0 | 0
1 | 0 | 0 |  | 0 | 0
1 | 0 | 1 |  | 0 | 0
1 | 1 | 0 |  | 1 | 1
1 | 1 | 1 |  | 0 | 0

## Slide 83: Complementation: Example
Find the complement of F(x,y,z) = xy’z’ + x’yz
  G = F’

## Slide 84: Complementation: Example
Find the complement of F(x,y,z) = xy’z’ + x’yz
  G = F’ = (xy’z’ + x’yz)’
  = (xy’z’)’ • (x’yz)’ DeMorgan
  = (x’+y+z) • (x+y’+z’) DeMorgan again
Note:
  Complement of F: dual(F)  complement all literals

## Slide 85: Complement of a Function
• ↔ +
1 ↔ 0
X ↔ X’
  Interchange 1s to 0s in the truth table column showing F.
  The complement of a function IS NOT THE SAME as the dual of a function.

## Slide 86: De Morgan’s Law for a Complex Expression
Example:
  ((A + B’).C’.D + EF)’
  =

## Slide 87: De Morgan’s Law for a Complex Expression
Example:
  ((A + B’).C’.D + EF)’
  = ((A’.B) + C + D’) . (E’ + F’)
Note:
  Don’t change operator precedence

## Slide 88: Shannon Theorem
  F(x1,x2,…,xn) = x1.F(1,x2,…,xn) + x1’.F(0,x2,…,xn)
  F(x1,x2,…,xn) = [x1 + F(0,x2,…,xn)].[x1’+ F(1,x2,…,xn)]

## Slide 89: Boolean vs. Ordinary Algebra
Some of Boolean Algebra are not true for ordinary algebra
Example:
True in ordinary algebra
Not True in Boolean algebra
Example:
True in ordinary algebra
Not True in Boolean algebra
Example:
True in both ordinary and
Boolean algebra
Some of Boolean Algebra properties are true for ordinary algebra too.

## Slide 90: Relationship Among Representations
Theorem:
  Any Boolean function that can be expressed as a truth table can be written as an expression in Boolean Algebra using AND, OR, NOT.
How do we convert from one to the other?
Optimizations?
covered
covered
covered
covered

## Slide 91: Ckt (Gate) to Truth Table
  Circuit to be analyzed:
  Consider all possible combinations of inputs

## Slide 92: Ckt to Boolean + Boolean to TT
Logic Expression :
Circuit of logic gates :
Logic Evaluation : A=B=C=1, D=E=0

## Slide 93: Boolean to Ckt
Combinational Circuit Design:
F = A’ + B•C’ + A’•B’
  connect input signals and logic gates:
    Circuit input signals  from function variables (A, B, C)
    Circuit output signal  function output (F)
    Logic gates  from logic operations
A
B
C
F

## Slide 94: Minterms and Maxterms
Minterm:
  a product term in which all the variables appear exactly once, either complemented or uncomplemented
Maxterm:
  a sum term in which ….
  Minterms and Maxterms are easy to denote using a truth table.
x | y | z |  | Minterm | Maxterm
0 | 0 | 0 |  | x’y’z’ = m0 | x+y+z = M0
0 | 0 | 1 |  | x’y’z = m1 | x+y+z’ = M1
0 | 1 | 0 |  | x’yz’ = m2 | x+y’+z = M2
0 | 1 | 1 |  | x’yz = m3 | x+y’+z’= M3
1 | 0 | 0 |  | xy’z’ = m4 | x’+y+z = M4
1 | 0 | 1 |  | xy’z = m5 | x’+y+z’ = M5
1 | 1 | 0 |  | xyz’ = m6 | x’+y’+z = M6
1 | 1 | 1 |  | xyz = m7 | x’+y’+z’ = M7
Observe that: mj = Mj’

## Slide 95: Canonical Forms: Unique
  Any Boolean function F( ) can be expressed as a unique sum of minterms (and a unique product of maxterms)
  In other words, every function F() has two canonical forms:
    Canonical Sum-Of-Products (sum of minterms)
    Canonical Product-Of-Sums (product of maxterms)

## Slide 96: Canonical Forms (cont.)
Canonical Sum-Of-Products:
  The minterms included are those mj’s such that F( ) = 1 in row j of the truth table for F( ).
Canonical Product-Of-Sums:
  The maxterms included are those Mj’s such that F( ) = 0 in row j of the truth table for F( ).

## Slide 97: Example
  f1(a,b,c) = m1 + m2 + m4 + m6
  = a’b’c + a’bc’ + ab’c’ + abc’
  f1(a,b,c) = M0 • M3 • M5 • M7
  = (a+b+c)•(a+b’+c’)• (a’+b+c’)•(a’+b’+c’).
a | b | c |  | f1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 2 | 1
0 | 1 | 1 | 3 | 0
1 | 0 | 0 | 4 | 1
1 | 0 | 1 | 5 | 0
1 | 1 | 0 | 6 | 1
1 | 1 | 1 | 7 | 0

## Slide 98: Shorthand: ∑ and ∏
f1(a,b,c) = ∑ m(1,2,4,6),
  m1+ m2 + m4 + m6.
f1(a,b,c) = ∏ M(0,3,5,7),
  M0 . M3 . M5 . M7.

## Slide 99: Conversion Between Canonical Forms
  Replace ∑ with ∏ (or vice versa)
  Replace those j’s that appeared in the original form with those that do not.
Example:
  f1(a,b,c) = a’b’c + a’bc’ + ab’c’ + abc’ = m1 + m2 + m4 + m6 = ∑(1,2,4,6) = ∏(0,3,5,7) = (a+b+c)•(a+b’+c’)•(a’+b+c’)•(a’+b’+c’)

## Slide 100: Standard Forms (NOT Unique)
  Standard forms are “like” canonical forms,
    Not all variables need appear in the individual product (SOP) or sum (POS) terms.
Example:
  f1(a,b,c) = a’b’c + bc’ + ac’ is a standard sum-of-products form
  f1(a,b,c) = (a+b+c)•(b’+c’)•(a’+c’) is a standard product-of-sums form.

## Slide 101: Alternative Implementations
Canonical Sum of Products
Minimized Sum of Products
Canonical Products of Sums
A
B
F
2
F
3
F
1
C
F(A,B,C) = PM(0,1,2)
= (A + B + C) (A + B + C') (A + B' + C)
F = A' B C + A B' C' + A B' C + A B C' + A B C
F(A,B,C) = Sm(3,4,5,6,7)
A + B C

## Slide 102: Conversion of SOP from standard to canonical
  Expand non-canonical terms by inserting equivalent of 1 in each missing variable
    x: (x + x’) = 1
  Remove duplicate minterms
  f1(a,b,c) = a’b’c + bc’ + ac’ = a’b’c + (a+a’)bc’ + a(b+b’)c’ = a’b’c + abc’ + a’bc’ + abc’ + ab’c’ = a’b’c + abc’ + a’bc + ab’c’

## Slide 103: Conversion of POS from standard to canonical
  Expand noncanonical terms by adding 0 in terms of missing variables (e.g., xx’ = 0) and using the distributive law
  Remove duplicate maxterms
  f1(a,b,c) = (a+b+c)•(b’+c’)•(a’+c’) = (a+b+c)•(aa’+b’+c’)•(a’+bb’+c’) = (a+b+c)•(a+b’+c’)•(a’+b’+c’)• (a’+b+c’)•(a’+b’+c’) = (a+b+c)•(a+b’+c’)•(a’+b’+c’)•(a’+b+c’)

## Slide 104: More Logic Gates
NAND:
  NOT-AND
    Its output = 1, only if both inputs are not 1.
    (A • B)’
  has traditionally been the universal gate in digital circuits.
    It is simple to implement in hardware and can be used to construct the other gates.
A | B | (A.B)’
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 105: More Logic Gates
NOR:
  NOT-OR
    Its output = 1, only if no input is 1.
    (A + B)’
  Can be a universal gate.
A | B | (A+B)’
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 106: More Logic Gates
XOR:
  Inequality
    Its output = 1, only if exactly one input is 1.
    (A  B)
A | B | A XOR B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
(A  B) = A.B’ + A’.B

## Slide 107: More Logic Gates
3-input XOR:
    Its output = 1, only if one or three inputs are 1.
    (A  B  C)
A | B | C | A XOR B XOR C
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 108: More Logic Gates
XNOR:
  Equality
    Its output = 1, only both inputs are equal.
    (A  B)’
A | B | A XNOR B
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
(A  B)’ = A.B + A’.B’

## Slide 109: Theorems for XOR

## Slide 110: Problem Solving
  More often, we describe a logic function using the English-language connectives “and,” “or,” and “not.”
Example: CE Lift
  The MOVE output is 1 if
    a button in a floor (OUTSIDEB) is 1, and OPENB button is 0 and door lift is closed (CLOSED = 1)
    or a button inside the lift (INSIDEB) is 1 and door lift is closed (CLOSED = 1)
  OUTSIDEB is 1 if
    OUTBUTTON1 is 1 or OUTBUTTON2 is 1 or OUTBUTTON3 is 1
  INSIDEB is 1 if
    KEY1 is 1 or KEY2 is 1 or KEY3 is 1

## Slide 111: Problem Solving
  Sometimes we have to work with imprecise word descriptions of logic functions,
Example:
  “The ERROR output should be 1 if the GEAR, CLUTCH, and BRAKE inputs are inconsistent.”
  Truth-table approach is best
    It allows us to determine the output required for every input combination, based on our knowledge and understanding of the problem environment
    e.g., the gear cannot be applied unless the clutch is pressed.

## Slide 112: Example
A 4-bit Prime Number Detector
F = SN3,N2,N1,N0(1, 2, 3, 5, 7, 11, 13)
=N3¢.N2¢.N1¢.N0 + N3¢.N2¢.N1.N0¢ + N3¢.N2¢.N1.N0+ N3¢.N2.N1¢.N0 + N3¢.N2.N1.N0 + N3.N2¢.N1.N0 + N3.N2.N1¢.N0
N3¢.N1¢.N0 + N3¢.N2¢.N1 + N3¢.N2.N1.N0 + N3.N2¢.N1.N0 + N3.N2.N1¢.N0
…
براي عبارات پيچيده، کار بهينه سازي سخت تر ميشود.
روشي سيستماتيک و آسان تر: نقشة کارنو
  شما را از جبر بول بي نياز نمي کند.

## Slide 113: 7-Segment Decoder
Seven-segment display:
  7 LEDs (light emitting diodes), each one controlled by an input
  1 means “on”, 0 means “off”
  Display digit “3”?
    Set a, b, c, d, g to 1
    Set e, f to 0
d
a
b
c
e
f
g

## Slide 114: 7-Segment Decoder
C
5
C
0
C
6
C
3
C
4
C
1
C
2
C
0
C
1
C
2
C
3
C
4
C
5
C
6
4-bit Binary-to-7-segment
control signal
decoder
A
B
C
D

## Slide 115: 7-Segment Decoder
7-Segment Decoder:
  Input is a 4-bit binary code  4 inputs (A, B, C, D).
  Output is a 7-bit code (a,b,c,d,e,f,g) that allows for the decimal equivalent to be displayed.
Example:
  Input: 0000
  Output: 1111110 (a=b=c=d=e=f=1, g=0)
d
a
b
c
e
f
g

## Slide 116: Binary-to-7Segment Truth Table
11100X0
0111
7
X011111
0110
6
1011011
0101
5
0110011
0100
4
1111001
0011
3
1101101
0010
2
0110000
0001
1
1111110
0000
0
abcdefg
ABCD
Digit
abcdefg
ABCD
Digit
XXXXXXX
1111
XXXXXXX
1110
XXXXXXX
1101
XXXXXXX
1100
XXXXXXX
1011
XXXXXXX
1010
111X011
1001
9
1111111
1000
8
??

## Slide 117: Binary-to-7Segment Truth Table
0111
7
0110
6
1011011
0101
5
0110011
0100
4
1111001
0011
3
1101101
0010
2
0110000
0001
1
1111110
0000
0
abcdefg
ABCD
Digit
abcdefg
ABCD
Digit
XXXXXXX
1111
XXXXXXX
1110
XXXXXXX
1101
XXXXXXX
1100
XXXXXXX
1011
XXXXXXX
1010
1001
9
1111111
1000
8
??
1011111
1110000
1110011

## Slide 118: Incompletely Specified Functions
These input patterns should
never be encountered in practice
associated output values are
"Don't Cares"
Off-set of W
On-set of W
Don't care (DC) set of W
Don’t Care:
  We don’t care about the output values for some intput patterns.
  this fact can be exploited during circuit minimization!
Example:
  BCD incrementer:

## Slide 119: Don't Cares and Canonical Forms
Z = m0 + m2 + m4 + m6 + m8 + d10 + d11 + d12 + d13 + d14 + d15
Z = m(0, 2, 4, 6, 8) + d(10, 11, 12 ,13, 14, 15)
Z = M1 • M3 • M5 • M7 • M9 • D10 • D11 • D12 • D13 • D14 • D15
Z= M(1, 3, 5, 7, 9) • D(10, 11, 12, 13, 14 ,15)
Canonical Representations of the BCD Incrementer: