## Slide 1: Sequential Circuit Design

## Slide 2: Design Procedure
  Specification
  Formulation
    Obtain a state diagram or state table
  State Assignment
    Assign binary codes to the states
  Flip-Flop Input Equation Determination
    Select flip-flop types
    Derive flip-flop equations from next state entries in the table
  Output Equation Determination
    Derive output equations from output entries in the table
  Optimization
    Optimize the equations
  Technology Mapping
    Find circuit from equations and map to flip-flops and gate technology
  Verification
    Verify correctness of final design

## Slide 3: Typical Sequential Circuit
State Register
C1
x(t)
s(t+1)
s(t)
z(t)
clock
present
state
present
inputs
next
state
C2
Mealy Machine

## Slide 4: Typical Sequential Circuit
C
D
Q
Q
C
D
Q
Q'
y
x
A
A’
B
CP
Next State
Output
Example

## Slide 5: Sequence Detector
101 sequence Detector
X = | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0
Z = | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
(time: | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15)

## Slide 6: Design of 101 Sequence Detector
State Diagram:
1/0

## Slide 7: Design of 101 Sequence Detector
State Diagram (final):

## Slide 8: Design of 101 Sequence Detector
State Table:
Present state |  | Next State |  | Present Output | 
 |  | X = 0 | X = 1 | X = 0 | X =1
S0 S1 S2 |  | S0 S2 S0 | S1 S1 S1 | 0 0 0 | 0 0 1
AB |  | A+ B+ |  | Z | 
 |  | X = 0 | X = 1 | X = 0 | X =1
00 01 10 |  | 00 10 00 | 01 01 01 | 0 0 0 | 0 0 1
State Table with State Assignment:
DA
DB

## Slide 9
AB |  | A+ B+ |  | Z | 
 |  | X = 0 | X = 1 | X = 0 | X =1
00 01 10 |  | 00 10 00 | 01 01 01 | 0 0 0 | 0 0 1
AB |  |  | 
 | x | A+ B+ | Z
00 00 01 01 10 10 | 0 1 0 1 0 1 | 00 01 10 01 00 01 | 0 0 0 0 0 1

## Slide 10: Design of Sequence Detector
Derive Boolean Equations:
A
B
A
B
X
00
01
11
10
0
1
0
0
1
0
X
X
0
0
DA = X’.B
A
B
A
B
X
00
01
11
10
0
1
0
1
0
1
X
X
0
1
DB = X
0
A
B
A
B
00
01
11
10
0
1
0
0
0
X
X
0
1
Z = X.A

## Slide 11: Design of Sequence Detector
Compare with Typical Mealy Machine
State Register
C1
x(t)
s(t+1)
s(t)
z(t)
clock
present
state
present
inputs
next
state
C2

## Slide 12: Design of Sequence Detector
A Moore Sequence Detector:
State Register
C1
x(t)
s(t+1)
s(t)
z(t)
clock
present
state
present
inputs
next
state
C2

## Slide 13: Sequence Detector
101 sequence Detector
X = | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0
Z = | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
(time: | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15)

## Slide 14: Design of a Sequence Detector
S0: start
S1: got 1
S2: got 10
S3: got 101

## Slide 15: Design of a Sequence Detector
S0: start
S1: got 1
S2: got 10
S3: got 101

## Slide 16: Design of a Sequence Detector
State Table
Present state |  | Next State |  | Present Output (Z)
 |  | X = 0 | X = 1 | 
S0 S1 S2 S3 |  | S0 S2 S0 S2 | S1 S1 S3 S1 | 0 0 0 1
AB |  | A+ B+ |  | Z
 |  | X = 0 | X = 1 | 
00 01 11 10 |  | 00 11 00 11 | 01 01 10 01 | 0 0 0 1
Transition Table with State assignment
DA
DB

## Slide 17: State Diagram Development
To develop a sequence recognizer state diagram:
  Construct some sample input and output sequences to make sure that you understand the problem statement.
  Begin in an initial state in which NONE of the initial portion of the sequence has occurred (typically “reset” state).
  Add a state that recognizes that the first symbol has occurred.
  Add states that recognize each successive symbol occurring.
  Each time you add an arrow to the state graph, determine it can go to one of the previously defined states or whether a new state must be added
  The final state represents the input sequence occurrence.
  Add state transition arcs which specify what happens when a symbol not in the proper sequence has occurred.
  Check your state graph for completeness and non-redundant arcs.
  When your state graph is complete, test it by applying the input sequences formulated in part1 and making sure the output sequences are correct

## Slide 18: State Assignment
  Each of the m states must be assigned a unique code.
  Minimum number of bits required is n such that n ≥ log2 m where x is the smallest integer ≥ x.
  There are 2n - m unused states.
  (There are useful state assignments that use more than the minimum number of bits).

## Slide 19: State Assignment: Example 2
  How many assignments of codes with a minimum number of bits?
    4  3  2  1 = 24
  Does code assignment make a difference in cost?
Present
State
Next State
x=0 x=1
Output
x=0 x=1
A
A B
0 0
B
A C
0 0
C
D C
0 0
D
A B
0 1

## Slide 20: State Assignment: Example 2
  Assignment 1:
    A = 00, B = 01, C = 10, D = 11
  The resulting coded state table:
Present State | Next State x = 0 x = 1 |  | Output x = 0 x = 1 | 
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 0 | 0 | 0
1 0 | 1 1 | 1 0 | 0 | 0
1 1 | 0 0 | 0 1 | 0 | 1

## Slide 21: Flip-Flop Input and Output Equations: Example 2 (version 1)
A
B
A
B
X
00
01
11
10
0
1
0
0
0
1
0
0
1
1
DA = A.B’ + X.A’.B
A
B
A
B
X
00
01
11
10
0
1
0
1
0
0
0
1
1
0
DB = X’.A.B’ + X.A’.B’+X.A.B
  Assume D flip-flops
  Interchange the bottom two rows of the state table, to obtain K-maps for DA, DB, and Z:

## Slide 22: Flip-Flop Input and Output Equations: Example 2 (version 1)
A
B
A
B
X
00
01
11
10
0
1
0
0
0
0
0
1
0
0
Z = A.B.X
Gate Input Cost = 22

## Slide 23: State Assignment: Example 2
  Assignment 2:
    A = 00, B = 01, C = 11, D = 10
  The resulting coded state table:
Present State | Next State x = 0 x = 1 |  | Output x = 0 x = 1 | 
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 1 | 0 | 0
1 1 | 1 0 | 1 1 | 0 | 0
1 0 | 0 0 | 0 1 | 0 | 1

## Slide 24: Flip-Flop Input and Output Equations: Example 2 (version 2)
A
B
A
B
X
00
01
11
10
0
1
0
0
0
1
1
1
0
0
DA = A.B + X.B
A
B
A
B
X
00
01
11
10
0
1
0
1
0
1
0
1
0
1
DB = X
  Assume D flip-flops
  Interchange the bottom two rows of the state table, to obtain K-maps for DA, DB, and Z:

## Slide 25: Flip-Flop Input and Output Equations: Example 2 (version 2)
A
B
A
B
X
00
01
11
10
0
1
0
0
0
0
0
0
0
1
Z = A.B’.X
Gate Input Cost = 9
Select this state assignment

## Slide 26: Implementation
Library:
  D Flip-flops with Reset (not inverted)
  NAND gates with up to 4 inputs and inverters
Initial Circuit:
Clock
D
D
C
R
Y2
Z
C
R
Y1
X
Reset

## Slide 27: Technology Mapping
Clock
D
D
C
R
Y2
Z
C
R
Y1
X
Reset

## Slide 28: Example : Vending Machine
General Machine Concept:
  Deliver package of gum after 15 cents deposited
  Single coin slot for dimes (10¢), nickels (5¢)
  No change

## Slide 29: Example : Vending Machine
Step 1: Understand the problem:
  Draw a picture
Vending
Machine
FSM
5¢
10¢
Reset
Clk
Open
Coin
Sensor
Gum
Release
Mechanism

## Slide 30: Example : Vending Machine
Step 2: Draw state diagram:
  All possible sequences
    Inputs: N, D, reset
    Output: open
Reset
N
N
N
D
D
N
D
[open]
[open]
[open]
[open]
S0
S1
S2
S3
S4
S5
S6
S8
[open]
S7
D
Dime: 10¢
Nickel: 5¢
Notes:
  If neither N nor D, goes to itself.
  Both N and D is not possible.

## Slide 31: Example : Vending Machine
Step 3: State minimization:
  Reuse states whenever possible
Dime: 10¢
Nickel: 5¢
Reset
N
N
N, D
[open]
15¢
0¢
5¢
10¢
D
D

## Slide 32: Example : Vending Machine
Step 4: Symbolic State table:
Reset
N
N
N, D
[open]
15¢
0¢
5¢
10¢
D
D
Present
State
0¢
5¢
10¢
15¢
D
0
0
1
1
0
0
1
1
0
0
1
1
X
N
0
1
0
1
0
1
0
1
0
1
0
1
X
Inputs
Next
State
0¢
5¢
10¢
X
5¢
10¢
15¢
X
10¢
15¢
15¢
X
15¢
Output
Open
0
0
0
X
0
0
0
X
0
0
0
X
1
From 15¢ state, you may want to go to reset state

## Slide 33: Example : Vending Machine
Step 5: State encoding:
Next State
D
1
D
0
0
0
0 1
1 0
X X
0 1
1 0
1 1
X X
1 0
1 1
1 1
X X
1 1
1 1
1 1
X X
Present State
Q
1
Q
0
0
0
0 1
1 0
1 1
D
0
0
1
1
0
0
1
1
0
0
1
1
0
0
1
1
N
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
Inputs
Output
Open
0
0
0
X
0
0
0
X
0
0
0
X
1
1
1
X

## Slide 34: Example : Vending Machine
Step 6: Choose FF for implementation:
  DFF easiest
D1 = Q1 + D + Q0 N
D0 = N Q0’ + Q0 N’ + Q1 N + Q1 D
OPEN = Q1 Q0
8 Gates
CLK
OPEN
CLK
Q
0
D
R
Q
Q
D
R
Q
Q
\
Q
1
\reset
\reset
\
Q
0
\
Q
0
Q
0
Q
0
Q
1
Q
1
Q
1
Q
1
D
D
N
N
N
\
N
D
1
D
0
K-map for D1
Q1 Q0
D N
Q1
Q0
D
N
0 0 1 1
0 1 1 1
X X X X
1 1 1 1
K-map for D0
Q1 Q0
D N
Q1
Q0
D
N
0 1 1 0
1 0 1 1
X X X X
0 1 1 1
K-map for Open
Q1 Q0
D N
Q1
Q0
D
N
0 0 1 0
0 0 1 0
X X X X
0 0 1 0

## Slide 35: Equivalence of Moore and Mealy Machines
Outputs are associated
with State
Outputs are associated
with Transitions
Moore
Machine
Reset
N
N
N+D
[1]
15¢
0¢
5¢
10¢
D
[0]
[0]
[0]
D
N D + Reset
Reset
Reset
N D
N D
Mealy
Machine
Reset/0
N/0
N/0
N+D/1
15¢
0¢
5¢
10¢
D/0
D/1
(N D + Reset)/0
Reset/0
Reset/1
N D/0
N D/0

## Slide 36: Using Other FFs for Design
Characteristic Table:
  defines the next state of the flip-flop in terms of flip-flop inputs and current state.
    Used in Circuit Analysis
Excitation Table:
  defines the flip-flop input variable values as function of the current state and next state.
    Used in Circuit Design

## Slide 37: SR FF Tables
Characteristic Table:
Excitation Table:
0
0
1
1
Operation
S
0
1
0
1
R
No change
Reset
Set
Undefined
0
1
?
Q(t
+
1)
Q(t)
Operation
No change / Reset
Set
Reset
No change / Set
S
X
0
1
0
Q(t+
1)
0
1
1
0
Q(t)
0
0
1
1
R
X
0
1
0

## Slide 38: DFF Tables
Characteristic Table:
D
0
1
Operation
Reset
Set
0
1
Q(t
1)
+
Excitation Table:
D
1
0
1
0
Q(t+
1)
0
1
1
0
Q(t)
0
0
1
1

## Slide 39: JK FF Tables
0
0
1
1
No change
Set
Reset
Complement
Operation
J
0
1
0
1
K
0
1
Q(t+1)
Q(t)
Q(t)
Q(t+1)
0
1
1
0
Q(t)
0
0
1
1
Operation
X
X
0
1
K
0
1
X
X
J
No change / Reset
Set / Toggle
Reset / Toggle
No Change / Set
Characteristic Table:
Excitation Table:

## Slide 40: T FF Tables
Characteristic Table:
Excitation Table:
No change
Complement
Operation
0
1
T
Q(t+1)
Q(t)
Q(t)
Q(t+1)
0
1
1
0
Q(t)
0
0
1
1
Operation
0
1
0
1
T
No change
Toggle
Toggle
No Change

## Slide 41: Example
Design by DFF

## Slide 42: Example
A(t + 1) = DA(A,B,X) =  m(2,4,5,6)
B(t + 1) = DB(A,B,X) =  m(1,3,5,6)
Y(A,B,X) =  m(1,5)
DA = AB + BX
A
A
DB = AX + BX + ABX
A
BX
Y = BX
BX
BX

## Slide 43: Example
  Logic Diagram for Circuit with D Flip-Flops

## Slide 44: Example
Design by JK FF
Q(t+1)
0
1
1
0
Q(t)
0
0
1
1
Operation
X
X
0
1
K
0
1
X
X
J
No change/reset
Set/Toggle
Reset/Toggle
No Change/set
  Don’t cares
    lead to simpler combinational circuit

## Slide 45: Example: Boolean Equations
JA = BX JB = X
KA = BX KB = AX + AX

## Slide 46: Example: Logic Diagram